## Slide 1: Series and parallel resistances
Notes: This lesson presents the equations for calculating total (equivalent) resistance for series and parallel combinations of resistors, and provides practice in calculating total resistance. In the hands-on investigation, students combine bulbs in series and parallel, and relate the effect on bulb brightness to the circuit’s total resistance.

## Slide 2: Objectives
Calculate the equivalent resistance for resistors connected in both series and parallel combinations.
Construct series and parallel circuits of bulbs (resistors).
Observe and explain relative bulb brightness in series and parallel circuits.
Notes: The next set of slides will preview the assessments for the first objective. Objectives two and three will be assessed within the investigation itself.

## Slide 3: Assessment
Two resistors with resistances of 10 Ω and 30 Ω are connected in series with a 20 volt battery.
  What is the equivalent resistance of the circuit?
  b) What is the current flow through the circuit?
Notes: These next two slides preview the assessments for each objective. These assessments will be administered at the end or within the body of the lesson. This question assess the series combination of resistors.

## Slide 4: Assessment
Two resistors with resistances of 10 Ω and 30 Ω are connected in parallel with a 20 volt battery.
  What is the equivalent resistance of the circuit?
  b) What is the current flow through the circuit?
Notes: This question assesses the parallel combination of resistors.

## Slide 5: Assessment
If you connect two identical resistors as shown, will they together draw more or less current than one of the resistors alone?
Notes: This question assesses the parallel combination of resistors.

## Slide 6: Physics terms
series circuit
parallel circuit
equivalent resistance
Notes: Students have already been exposed to series and parallel arrangements of batteries, so these concepts are not completely new. It is important that they develop a clear understanding of the term equivalent resistance. Equivalent resistance is the total effective resistance of a combination of resistors.

## Slide 7: Equations
Equivalent resistance for resistors connected in series
Equivalent resistance for resistors connected in parallel
Notes: The e-book contains interactive calculators to help the students explore the use of these equations.

## Slide 8
A series circuit has only one path for the flow of electric current.
Series circuits
I
I
I
Notes: Ask: “What must be true about the current through each of these resistors?”
Answer: the same amount of current must flow through each resistor in series.
Try to get the students to come up with the answer to the question on the slide.

## Slide 9
Parallel circuits
In a parallel circuit the electric current can split apart and come back together again.
V
V
Notes: Analogies are helpful in getting this point across. It is like adding lanes to a highway so that the vehicles can flow

## Slide 10
What are the advantages and disadvantages of series versus parallel circuits?
Investigation
In Investigation 17D you will create circuits of bulbs wired in parallel and series.

## Slide 11
Create a circuit using two batteries, one bulb, a switch, and any necessary wire modules.
Close the switch and observe the brightness of the bulb.
Investigation
Part 1: Connecting bulbs in series
Predict: What will happen to bulb brightness if you connect a second bulb in series?
Notes: Bulbs have resistance. Point out that in the first half of this investigation, students are creating a circuit with two resistors in series.
Ask them to predict: How will the brightness of two bulbs in series compare to the brightness of a single bulb.
Answer: they will be dimmer. Why?

## Slide 12
Create a circuit with two bulbs in series, as shown in the circuit diagram. Compare the brightness of the two lamps to the previous circuit with one lamp.
Investigation
Part 1: Connecting bulbs in series

## Slide 13
What property makes this a series circuit?
How bright are the two bulbs in series compared to a single bulb circuit? Why?
Unscrew one bulb from the series circuit. What happens to the other bulb? Why?
Investigation
Questions for Part 1

## Slide 14
Which arrangement has more current flow through the lamps?
Investigation
Part 2: Connecting bulbs in parallel
Create a circuit with two bulbs in parallel, as shown in the circuit diagram.
Compare the brightness of the bulbs in this circuit to the prior circuit with two bulbs in series.
Notes: First ask them to predict: How will the brightness of two lamps in parallel compare to the brightness of a single lamp.
Answer: they will have the same brightness. Why?

## Slide 15
What property makes this a parallel circuit?
How bright are the parallel bulbs compared to the series bulbs? Compared to the single bulb? Why?
Unscrew one bulb from the parallel circuit. What happens to the brightness of the other bulb? Why?
Is a series or parallel circuit better for connecting a string of lights? Why?
Investigation
Questions for Part 2
Notes: Removing the lamp in a series circuit creates an open circuit situation, stopping all flow of current in the circuit. Point out that in the parallel circuit, the second lamp is still wired to the battery, so current can still flow though that branch.

## Slide 16
Designing a circuit
Design a circuit of three lamps that combines series and parallel arrangements.
Sketch the circuit diagram.
Predict the relative bulb brightness.
Build the circuit and test your predictions.
Is there a second way you could have designed your circuit?
Notes: There are two different circuits that satisfy this requirement.

## Slide 17
Series circuits
The battery and the resistors in these circuits are identical.
What is different about these circuits?
Notes: Ask: What must be true about the current through each of these resistors?
Answer: the same amount of current must flow through each resistor in series.
Try to get the students to come up with the answer to the question on the slide.

## Slide 18
The circuit with 3 resistors is 3 times harder for the current to flow through.
Series circuits
When you add resistors in series, equivalent resistance increases and current flow decreases: I3 < I2 < I1
I1
I2
I3

## Slide 19
What is “equivalent resistance”?
  Equivalent resistance is the total combined resistance of a group of resistors.
  Equivalent resistance has the value of a single resistor that could replace all the resistors in a circuit, while keeping total current through the circuit the same.
Equivalent resistance

## Slide 20
  . . . so they will have the same total current, I.
These two circuits have the same total resistance . . .
Equivalent resistance
Notes: This is an example of equivalent resistance. Again, we are assuming that the voltage source is the same, and all resistors are identical.

## Slide 21
For resistors in series, the equivalent resistance is simply the sum of the individual resistances.
Equivalent resistance: series
Notes: When you add resistors in series, the total resistance INCREASES. Therefore, when you add resistors in series, the current DECREASES.
This is because each resistor added in series makes it harder for the current to flow along that branch.

## Slide 22
Click this interactive.
Exploring the ideas
Notes: The interactive calculators in the e-Book will aid in practicing the calculations, and help students differentiate between series and parallel combinations of resistors.

## Slide 23
A 10 Ω resistor, a 15 Ω resistor, and a 5 Ω resistor are connected in series.
What is the equivalent resistance of this arrangement?
Engaging with the concepts
10
15
5

## Slide 24
A 10 Ω resistor, a 15 Ω resistor, and a 5 Ω resistor are connected in series.
What is the equivalent resistance of this arrangement?
Engaging with the concepts
10 Ω + 15 Ω + 5 Ω = 30 Ω
10
15
5
30

## Slide 25
Two strings of tree lights, each with a resistance of 150 Ω, are connected together in series.
What is the Req?
Engaging with the concepts
150
150
0

## Slide 26
Two strings of tree lights, each with a resistance of 150 Ω, are connected together in series.
What is the Req?
Engaging with the concepts
150
150
0
300
300 Ω
When you add resistors in series, does Req increase or decrease?
Does total current increase or decrease?
Notes: Remind them: I = V/R. (Answer: if total resistance increases, the current decreases.)

## Slide 27
Two strings of tree lights, each with a resistance of 150 Ω, are connected together in series.
What is the Req?
Engaging with the concepts
150
150
150
450
When you add resistors in series does Req increase or decrease?
Req increases
I decreases
Does total current increase or decrease?
300 Ω
Notes: More resistance means that less current can flow.

## Slide 28
Req = _______
Req = _______
What is the Req of each circuit?

## Slide 29
Req = 10 Ω
Req = 15 Ω
What is the Req of each circuit?
Notes: Review the use of Ohm’s law. V= IR so I = V/R

## Slide 30
Req = 10 Ω
Req = 15 Ω
How much current flows?
Notes: Review the use of Ohm’s law. V= IR so I = V/R

## Slide 31
1 A
0.67 A
How much current flows?
Notes: Point out that Ohm’s law can be applied to a single resistor, or a combination of resistors with an equivalent resistance.

## Slide 32
Parallel circuits
What is the Req for the parallel circuit? R 2R ½ R
A parallel circuit has more paths for electric current to flow. The circuit on the right lets twice as much current flow.
Notes: The voltage is the same for both circuits. Since more total current flows in the circuit on the right, it must have less total resistance.

## Slide 33
Parallel circuits
In the circuit with parallel resistors:
total current flow doubles because total resistance is halved.
What is the Req for the parallel circuit? R 2R ½ R
Notes: Analogies are helpful in getting this point across. It is like adding lanes to a highway so that the vehicles can flow.

## Slide 34
When you add resistors in parallel, total resistance goes DOWN.
To find the Req you must add the inverse of the resistances:
Equivalent resistance: parallel
Notes: When you add resistors in parallel, the equivalent resistance DECREASES and total current INCREASES.
So to find the equivalent resistance of resistors in parallel, we cannot simply add up the values. We need a new formula, shown here.

## Slide 35
Equivalent resistance: parallel
If you have two 4 Ω resistors in parallel, what is the equivalent resistance?
A. ½ Ω B. 2 Ω C. 4 Ω D. 8 Ω
Notes: Ask the students to use the formula to do this simple example in their heads, if possible, or step them through it.

## Slide 36
Equivalent resistance: parallel
If you have two 4 Ω resistors in parallel, what is the equivalent resistance?
A. ½ Ω B. 2 Ω C. 4 Ω D. 8 Ω
Don’t forget to flip the fraction at the end!
Notes: Point out that the answer, 2 ohms, is on the bottom. The answer is 2 ohms, not ½ ohm. Forgetting to flip the fraction is a very common error when adding resistors in parallel.

## Slide 37
Click this interactive.
Exploring the ideas
Notes: Often these problems are too hard to do in their heads. They need to use a calculator. The e-book contains an interactive calculator for exploring the use of this equation.

## Slide 38
Engaging with the concepts
A 10 Ω resistor and a 15 Ω resistor are connected in parallel. What is the Req of this arrangement?
10
15
Equivalent resistance
Notes: Before getting the answer on the next slide (6 ohms), help the students to realize that the answer must be LESS THAN 10 ohms. If any resistor is added in parallel to the 10 ohm resistor, the total resistance of the circuit must decrease. The total resistance of any parallel combination of resistors must be less than the resistance of any of the individual resistors. Knowing this will help the students check their work.

## Slide 39
Engaging with the concepts
A 10 Ω resistor and a 15 Ω resistor are connected in parallel. What is the Req of this arrangement? 6 ohms
10
15
Equivalent resistance
6
When resistors are connected in parallel, total resistance decreases.
Notes: If possible, shows students how easy it is to solve these problems by using the inverse (x^-1) button on their calculators.

## Slide 40
Engaging with the concepts
Two strings of lights, each with a resistance of 150 Ω, are connected together.
What is the Req when the strings are connected in parallel?
150
150
Equivalent resistance
Notes: Again, point out that the answer must be less than 150 ohms. Model using the calculator to get the solution (Answer: 75 ohms). The equivalent resistance for resistors connected in parallel is smaller than the individual resistances.

## Slide 41
Engaging with the concepts
Two strings of lights, each with a resistance of 150 Ω, are connected together.
What is the Req when the strings are connected in parallel? 75 Ω
150
150
Equivalent resistance
75
The total resistance is always less than any of the individual resistors added in parallel!
Notes: Follow-on question: What is the resistance of a 1 ohm and a 100 ohm resistor? 0.99 Ohms (less than 1 ohm)

## Slide 42
Req = ____
Req = ____
These are all 10 Ω resistors. What is the Req in each case?
Req = ____
What is the Req of each circuit?
Notes: Answers on next slide.

## Slide 43
Req = 10 Ω
Req = 5 Ω
These are all 10 Ω resistors. What is the Req in each case?
Req = 3.3 Ω
Adding resistors in parallel makes the total resistance decrease.
What is the Req of each circuit?
Notes: Answers on next slide.

## Slide 44
Req = 10 Ω
Req = 5 Ω
Apply Ohm’s law ( V = IR ) to find the total current through the battery.
Req = 3.3 Ω
I = ____
I = ____
I = ____
How much current flows?
Notes: V= IR so I = V/R. Answers on next slide.

## Slide 45
Req = 10 Ω
Req = 5 Ω
Req = 3.3 Ω
I = 3 A
I = 6 A
I = 9 A
How much current flows?
Apply Ohm’s law ( V = IR ) to find the total current through the battery.
Notes: Point out that the current through EACH resistor is 3 amps. If there are three resistors in parallel, there are 9 amps total.

## Slide 46
Analogy for resistors in series
What happens to the potential energy of the water as it passes through each water wheel?
How is this analogous to the voltage drops across each resistor?
Notes: Step the students through the water analogy. All the water flows past the first wheel to the second wheel and so on, just as ALL the current flows through each resistor.
Also note the changes in potential energy. The water loses a third of its gravitational potential energy passing through the first water wheel, then another third, and another.
Similarly, the electric charges lose a third of their electrical potential energy passing through the first resistor, then another third, and another (assuming the resistors are identical).

## Slide 47
Half as much current flows in the series circuit.
What are the voltage drops across the two resistors in series?
Voltage drops: resistors in series
Notes: Compare these two circuits. Note that that in the circuit on the right, the voltage of the battery must be shared between the two resistors. The battery “pumps up” the energy of the charges. The charges lose half their electrical potential energy in the first resistor (10 V), and the other half the energy in the second resistor (10 V) for a total voltage drop of 20 volt.

## Slide 48
Single resistor
Voltage drops: resistors in series
Resistor in series
10 V drop
10 V drop
Notes: Reinforce the analogy to the energy gains and losses in the water wheel circuit.

## Slide 49
Voltage drops: resistors in parallel
Twice as much current flows in the parallel circuit.
What are the voltage drops across the resistors in parallel?
Notes: Compare these two circuits. Each resistor is directly connected to the two ends of the battery, so each resistor has one volt applied to it. By Ohms law, I = V/R = 1 volt/1ohm = 1 amp.
If each resistor has 1 amp flowing through it, then a total of 2 amps must be flowing through the battery.

## Slide 50
Voltage drops: resistors in parallel
Each resistor in parallel has the full 20 V drop.
Single resistor
Resistor in parallel
4 A
4 A
20 V
drop
Notes: Each resistor is directly connected to the two ends of the battery, so each resistor is exposed to the full 20 V of the battery. The current splits, so each resistor gets only 4 amps, and Ohm’s law still holds.

## Slide 51: Assessment
Two resistors with resistances of 10 Ω and 30 Ω are connected in series with a 20 volt battery.
  What is the equivalent resistance of the circuit?
  What is the current flow through the circuit?
Notes: This slide assesses the student understanding of series resistor circuits.

## Slide 52: Assessment
Two resistors with resistances of 10 Ω and 30 Ω are connected in series with a 20 volt battery.
  What is the equivalent resistance of the circuit?
  What is the current flow through the circuit?
Notes: Series resisters simply add. Total resistance increases.

## Slide 53: Assessment
Two resistors with resistances of 10 Ω and 30 Ω are connected in series with a 20 volt battery.
  What is the equivalent resistance of the circuit?
  What is the current flow through the circuit?
Notes: Ohm’s law works for the entire circuit.

## Slide 54: Assessment
Two resistors with resistances of 10 Ω and 30 Ω are connected in parallel with a 20 volt battery.
  What is the equivalent resistance of the circuit?
Notes: This question assesses the parallel combination of resistors.

## Slide 55: Assessment
Two resistors with resistances of 10 Ω and 30 Ω are connected in parallel with a 20 volt battery.
  What is the equivalent resistance of the circuit? 7.5 Ω
  b) What is the current flow through the circuit?
Notes: Remind the students that they can use the e-book calculator. They need to remember to invert the final fraction.

## Slide 56: Assessment
Two resistors with resistances of 10 Ω and 30 Ω are connected in parallel with a 20 volt battery.
  What is the equivalent resistance of the circuit? 7.5 Ω
  b) What is the current flow through the circuit?
Notes: Notice the large current. When you add resistors in parallel, current increases.

## Slide 57: Assessment
If you connect two identical resistors as shown, will they together draw more or less current than one of the resistors alone?
Notes: This question assesses the parallel combination of resistors.

## Slide 58: Assessment
  They will draw more current, because they are connected in parallel. There are now two different but identical paths for electricity to flow, so the current doubles!
If you connect two identical resistors as shown, will they together draw more or less current than one of the resistors alone?
Notes: This question assesses the parallel combination of resistors.

## Slide 59
Assessment: bulbs in series
How bright are the bulbs in series compared to the single lamp? Why?
Notes: This last set of 8 slides provide the opportunity to review the lab results as a whole group, if desired.

## Slide 60
How bright are the bulbs in series compared to the single bulb? Why?
They are dimmer.
The total resistance increases, so the current decreases.
Assessment: bulbs in series

## Slide 61
When you remove one of the bulbs in series, what happens to the brightness of the other bulb? Why?
Assessment: bulbs in series

## Slide 62
When you remove one of the bulbs in series, what happens to the brightness of the other bulb? Why?
It goes out.
Removing the bulb results in an open circuit. No current flows.
Assessment: bulbs in series

## Slide 63
Assessment: bulbs in parallel
How bright are the bulbs in parallel compared to the series bulbs? Why?

## Slide 64
Assessment: bulbs in parallel
How bright are the bulbs in parallel compared to the series bulbs? Why?
The parallel bulbs are brighter.
They each get twice as much current as a series bulb.

## Slide 65
Assessment: bulbs in parallel
When you remove one of the bulbs in parallel, what happens to the brightness of the other bulb? Why?

## Slide 66
The other bulb remains on, and its brightness does not change.
The voltage and resistance of the bulb is unchanged so the current through it is unchanged.
Assessment: bulbs in parallel
When you remove one of the bulbs in parallel, what happens to the brightness of the other bulb? Why?