## Slide 1: Compound circuits

## Slide 2: Objectives
Identify compound circuits.
Calculate the equivalent resistance of a compound circuit.
Predict relative bulb brightnesses in a compound circuit.

## Slide 3: Assessment
1. Identify each circuit as a series, parallel, or compound arrangement.
A. B.
C. D.

## Slide 4: Assessment
For the circuit shown, calculate the equivalent resistance and current through the battery.

## Slide 5: Assessment
The bulbs in this circuit are identical. Rank the bulbs in order of brightness, from brightest to dimmest. Explain.
A
B
C

## Slide 6: Physics terms
compound circuit
voltage divider
equivalent resistance

## Slide 7: Equations
Ohm’s law
Equivalent resistance for series resistors
Electrical power
Equivalent resistance for parallel resistors

## Slide 8
There are series circuits.
Types of circuits
There are parallel circuits.
But some circuits are neither series nor parallel.

## Slide 9
A circuit that is a combination of series and parallel arrangements is called a compound circuit.
Compound circuits

## Slide 10
How do you find the Req of a compound circuit?
You need to take it step by step. What should you do first?
Compound circuit Req

## Slide 11
Start by identifying resistors that are simply in series or simply in parallel.
Compound circuit Req

## Slide 12
Start by identifying resistors that are simply in series or simply in parallel.
The 10-Ω and 15-Ω resistors are simply in parallel.
Find the Req for this section of the circuit:
Compound circuit Req

## Slide 13
Replace the parallel resistors with their equivalent resistance: 6 Ω.
What’s the next step?
Compound circuit Req

## Slide 14
Next: combine the two resistors in series:
The Req of this circuit is 26 Ω.
Compound circuit Req

## Slide 15
This circuit has an Req of 26 Ω and a 90-volt battery.
Analyzing compound circuits
90 V
What is the current through the battery?

## Slide 16
This circuit has an Req of 26 Ω and a 90-volt battery.
Analyzing compound circuits
What is the current through the battery?
90 V
3.5 A
Rank order the current flow through the resistors, from most to least.

## Slide 17
This circuit has an Req of 26 Ω and a 90-volt battery.
Analyzing compound circuits
What is the current through the battery?
90 V
3.5 A
Rank order the current flow through the resistors, from most to least.
Discuss your answer with the person next to you. Do you agree?

## Slide 18
This circuit has an Req of 26 Ω and a 90-volt battery.
Analyzing compound circuits
90 V
What is the current through the battery?
Rank order the current flow through the resistors, from most to least.
3.5 A

## Slide 19
Another example
Hint: which resistors are simply in series or parallel?
What is the first step for finding the Req for this circuit of four resistors?

## Slide 20
What is the first step for finding the Req for this circuit of four resistors?
Another example
The 5-Ω and 10-Ω resistors are simply in series.
Replace this section of the circuit with its Req.

## Slide 21
What is the next step?
Another example

## Slide 22
The 15-Ω and 20-Ω resistors are in parallel. Replace this section of the circuit with its Req.
Another example
What is the next step?

## Slide 23
The 8.6-Ω and 30-Ω resistors are in series. Replace them with their Req.
Another example
The Req of the circuit is 39 Ω.

## Slide 24
In Investigation 17F you will build a compound circuit of three identical lamps.
Can you correctly predict the relative bulb brightness?
Investigation

## Slide 25
Investigation
Open the experiment file 17F_CompoundCircuits, and then power-on the Current and Voltage sensors and connect them to SPARKvue.

## Slide 26
For this circuit, predict the relative brightnesses of the lamps when the switch is closed and when it is open.
Part 1: Power dissipated by elements in a compound circuit
Investigation
Hint: Brightness is power. The power equations can help you.

## Slide 27
Construct the circuit.
Note the brightnesses of the lamps when the switch is open.
Close the switch and note how the brightnesses have changed.
Part 1: Power dissipated by elements in a compound circuit (continued)
Investigation

## Slide 28
Using Kirchhoff’s laws or an equation for power, justify your prediction for the relative brightness of the lamps when the switch is closed.
Did the brightness of lamp #1 change when the switch was closed? Explain.
Questions for Part 1
Investigation

## Slide 29
Add a voltage and current sensor to your circuit. Measure the voltage across and current through lamp #1 with the switch open and closed, then calculate the power. How do the measurements justify your explanation?
Questions for Part 1 (continued)
Investigation

## Slide 30
Did the brightness of lamp #2 change when the switch was closed? Explain.
Add a voltage and current sensor to your circuit. Measure the voltage across and current through lamp #2. Calculate the power. How do the measurements justify your explanation?
Questions for Part 1 (continued)
Investigation

## Slide 31
Part 2: Voltage divider
Investigation
Construct this circuit.
Measure the input voltage and the output voltage.

## Slide 32
Measure the input voltage and the output voltage for each resistor combination in the table.
Record your measurements in the table.
Part 2: Voltage divider (continued)
Investigation
Notes: Groups will need to borrow a second 10Ω resistor module from another group for the 10Ω - 10Ω combination, as the circuit kit only comes with one.

## Slide 33
Investigation
Questions for Part 2
How does the output voltage vary with R1 ?
How does it vary with R2 ?
Create a mathematical model to predict the output voltage using the input voltage and the two resistances.
Why is this circuit called a voltage divider?

## Slide 34: Assessment
1. Identify each circuit as a series, parallel, or compound arrangement.
A. B.
C. D.

## Slide 35: Assessment
1. Identify each circuit as a series, parallel, or compound arrangement.
A. B.
C. D.
compound series
compound
parallel

## Slide 36: Assessment
For the circuit shown, calculate the equivalent resistance and the current through the battery.

## Slide 37: Assessment
For the circuit shown, calculate the equivalent resistance and the current through the battery.

## Slide 38: Assessment
For the circuit shown, calculate the equivalent resistance and the current through the battery.

## Slide 39: Assessment
For the circuit shown, calculate the equivalent resistance and the current through the battery. Req = 50 Ω

## Slide 40: Assessment
For the circuit shown, calculate the equivalent resistance and the current through the battery. Req = 50 Ω
The current through the battery is 2 amps.

## Slide 41: Assessment
The bulbs in this circuit are identical. Rank the bulbs in order of brightness, from brightest to dimmest. Explain.
A
B
C

## Slide 42: Assessment
B is brightest. A and C are the same.
Brightness is power: P = I2R
The resistances are equal, so the bulb with more current is brighter.
A and C have equal current.
B has twice as much.
A
B
C
The bulbs in this circuit are identical. Rank the bulbs in order of brightness, from brightest to dimmest. Explain.