## Slide 1: Electrical power
Notes: This lesson defines electric power and examines household electrical systems and power usage. Students learn how power is related to current, voltage, and resistance, and how to calculate the power and energy use of common appliances. The lesson presents examples of power in electric circuit elements connected in both series and parallel combinations.

## Slide 2: Objectives
Use the equation for electrical power to solve circuit problems.
Understand basic concepts for home electricity usage and wiring.
Calculate the power used by electric circuit elements connected in both series and parallel combinations.

## Slide 3: Assessment
How much current flows through an incandescent light bulb that draws 40 W of power from a 120 V outlet?
Two 30 Ω resistors are connected in series to a 120 volt outlet.
  How much current flows through the circuit?
  What is the power output of this circuit?

## Slide 4: Assessment
Two 30 Ω resistors are connected in parallel to a 120 volt outlet.
  How much current flows through the circuit?
  What is the power output of this circuit?
How many kilowatt-hours are consumed by a 100 W incandescent light bulb if it is left on for an entire day and night?

## Slide 5: Physics terms
power
watt (W)
kilowatt-hour (kWh)
circuit breaker

## Slide 6
Investigation
Open the experiment file 17E_ElectricalPower and then power on the Current and Voltage sensors, and connect them to your software.

## Slide 7
Construct the circuit shown. Connect the voltage sensor across the 33 Ω resistor.
Begin recording data and close the switch. Continue recording data until the energy has reached 1 joule.
Repeat the experiment for the 100 Ω resistor.
Part 1: Resistors in Series
Investigation

## Slide 8
What happens to the power output for each resistor when the switch is closed? The energy measurement?
Which resistor recorded a higher power output? Why?
Which resistor consumed 1 joule of energy the fastest? How is this related to the power output?
Questions for Part 1
Investigation

## Slide 9
Fit a line to each energy versus time run.
How does the value of the slope compare to the power output?
What does the slope represent?
Questions for Part 1
Investigation

## Slide 10
Construct the circuit shown. Place the current sensor in series with the 33 Ω resistor and connect the voltage sensor across the 33 Ω resistor.
Begin recording data and close the switch. Continue recording data until the energy has reached 1 joule.
Repeat the experiment for the 100 Ω resistor.
Part 2: Resistors in Parallel
Investigation

## Slide 11
Does each resistor have the same power output as Part 1? Why or why not?
Which resistor has the higher power output? Is this the same as the results in Part 1? Why or why not?
Questions for Part 1
Investigation

## Slide 12
Do the resistors consume energy faster in series or in parallel? Why?
Does the power output of a device depend on the properties of the device, how it is wired in the circuit, or both?
Questions for Part 1
Investigation

## Slide 13: Equations
Power:
Electrical power:

## Slide 14
Power is the rate at which work is done or energy transferred or transformed.
Power

## Slide 15
The resting human body uses around 100 W of power—similar to an incandescent light bulb.
A desktop computer + monitor uses 150-200 W.
A laptop uses only 50 W.
Power: everyday examples

## Slide 16
Electrical power can be expressed in terms of current and voltage.
Electric energy is transferred by the electric current.
Electric energy may be converted into light (radiant energy), thermal energy (heat), or motion (mechanical energy).
Electrical power

## Slide 17
Voltage and current—volts and amps—together determine how much power is generated by a circuit component.
A 9-volt battery generates nine watts of power per amp of current.
Volts and amps

## Slide 18
A household outlet operates at 120 volts:
Why is electricity so useful?
It delivers 120 watts of power for every one amp of current.
A small electrical wire can deliver as much power as a horse: 1 hp = 746 W.
A household fuse box carries 60 amps or more, and as much power as several teams of horses!
Notes: Point out that one horsepower equals 746 watts. A little over 6 amps of current drawn from a typical outlet will provide as much power as a horse, actually slightly more than a typical horse!

## Slide 19
Click this interactive.
Exploring the ideas

## Slide 20
A student measures 0.50 A of current flowing through a 10 Ω resistor when 5.0 volts is applied.
How much power is dissipated by the resistor?
Engaging with the concepts
0.50
5.0
Power

## Slide 21
A student measures 0.50 A of current flowing through a 10 Ω resistor when 5.0 volts is applied.
How much power is dissipated by the resistor?
2.5 watts
Engaging with the concepts
0.50
5.0
Power
2.5
Notes: Point out that for this problem they did not need to know the resistance since they already knew the current.

## Slide 22
How much current flows through an incandescent bulb that draws 100 W of power from a 120 V outlet?
Engaging with the concepts
120
Current
100

## Slide 23
How much current flows through an incandescent bulb that draws 100 W of power from a 120 V outlet?
0.83 amps
Engaging with the concepts
120
Current
100
0.8333

## Slide 24
If you double the current in a circuit, how does the power change?
What if you double the voltage instead?
Engaging with the concepts
30
Power
2
60

## Slide 25
If you double the current in a circuit, how does the power change?
It doubles.
What if you double the voltage instead?
It doubles.
Engaging with the concepts
30
Power
4
120
Power is directly proportional to both current and voltage.

## Slide 26
A typical car may operate at 100 hp, or 75,000 watts. An electric car runs on batteries. Why can’t it run on a 1.5 V battery?
Engaging with the concepts
1.5
Current
75,000

## Slide 27
A typical car may operate at 100 hp, or 75,000 watts. An electric car runs on batteries. Why can’t it run on a 1.5 V battery?
A 1.5 V battery would need to source 50,000 A of current to supply that much power!
Engaging with the concepts
1.5
Current
75,000
50,000

## Slide 28
Redefining the volt
A 1 volt power supply generates 1 watt of power for each amp that flows.

## Slide 29
A typical car may operate at 100 hp, or 75,000 watts.
If a hybrid car runs on a 1.5 V battery, 50,000 A must flow!
Hybrid cars
If it runs on a 12 V battery, 6,520 A must flow!
With a 480 V battery, only 156 A must flow.

## Slide 30
Hybrid cars

## Slide 31
Incandescent bulbs are rated by the electrical power they consume, not by how much light they produce.
Power ratings of light bulbs
A 100 W incandescent bulb uses 100 W of electrical power.
Only 2 W is converted to light energy! The rest of the power is radiated away as heat.

## Slide 32
Incandescent bulbs are rated by the electrical power they consume, not by how much light they produce.
Power ratings of light bulbs
A 100 W incandescent bulb uses 100 W of electrical power.
Only 2 W is converted to light energy! The rest of the power is radiated away as heat.
Compact fluorescent bulbs produce the same light output with less power.

## Slide 33
How much current flows through 100 W incandescent versus CFL light bulbs?
Solving power problems

## Slide 34
How much current flows through 100 W incandescent versus CFL light bulbs?
Solving power problems

## Slide 35
How much current flows through 100 W incandescent versus CFL light bulbs?
Solving power problems

## Slide 36: Calculating total power
  Find the power of each element separately, and add them to get the total power.
  OR
  Calculate total power by multiplying the total current by the total voltage.
What if a circuit contains more than one element?
How do you calculate total power? Two ways:
Notes: The next set of slides used method 2.

## Slide 37: Power for resistors in parallel
Two 40 Ω resistors are connected in parallel to a 60-V battery.
How much total current flows through the circuit?
What is the power output of this circuit?
Notes: Point out that the TOTAL current is 3 amps. the current splits at the junction, so each resistor gets 1.5 amps.

## Slide 38: Power for resistors in parallel
Two 40 Ω resistors are connected in parallel to a 60-V battery.
How much total current flows through the circuit?
What is the power output of this circuit?
3.0 A
Notes: Point out that the TOTAL current is 3 amps. The current splits at the junction, so each resistor gets 1.5 amps.

## Slide 39: Power for resistors in parallel
Two 40 Ω resistors are connected in parallel to a 60-V battery.
How much total current flows through the circuit?
What is the power output of this circuit?
3.0 A
Notes: Point out that the TOTAL current is 3 amps. The current splits at the junction, so each resistor gets 1.5 amps.

## Slide 40
Two 40 Ω resistors are connected in series to a 60-V battery.
How much total current flows through the circuit?
What is the power output of this circuit?
Power for resistors in series

## Slide 41
Two 40 Ω resistors are connected in series to a 60-V battery.
How much total current flows through the circuit?
What is the power output of this circuit?
Power for resistors in series
0.75 A

## Slide 42
Two 40 Ω resistors are connected in series to a 60-V battery.
How much total current flows through the circuit?
What is the power output of this circuit?
Power for resistors in series
The power is lower in the series circuit!
0.75 A

## Slide 43
We all use electricity in our homes.
Electric power in the home
Are our homes wired in series or in parallel?
How do we make sure these circuits are safe?
How are we billed for the electricity we use?

## Slide 44
Remember this investigation?
Were the lamps brighter when connected in series or in parallel?
Would you want the lights all over your house to dim every time you turned on another light switch?
Which was series?
Parallel?
Home wiring: series or parallel?

## Slide 45
Homes are wired in parallel
Your house is wired in parallel so each appliance will have 120 volts.
Each device can be turned on and off without affecting the others.
If you turn off the hair dryer, you can still use the computer.
Notes: Ask students to point out the advantages of the parallel arrangement: each appliance can be turned on and off independently, and each appliance gets the full 120 V.

## Slide 46
Homes are wired in parallel
What happens when you turn on more appliances?

## Slide 47
Homes are wired in parallel
What happens when you turn on more appliances?
Because a house is wired in parallel, each additional appliance draws more current.

## Slide 48
Each added appliance draws more current from the same outlet.
If the total current exceeds the safety limit, then a circuit breaker will trip or a fuse will blow.
To fix the problem:
Unplug one or more appliances.
Replace a blown fuse or reset the circuit breaker by flipping the switch.
Too much current?
Notes: Point out the circuit breakers in the photo. Ask students if they have ever had to flip a circuit breaker back that was tripped. Fuses and circuit breakers limit the total current flow through the household circuits, which protects the wires from overheating and causing a fire.

## Slide 49
When you pay an electric bill, what are you actually paying for?
electrons? voltage? current? energy? power?
What units do electric companies use to figure out the bill?
What are you buying?
Notes: Give the students time to think about this and perhaps locate the unit of kWh on this bill.

## Slide 50
Your local power company charges homeowners and companies in kilowatt-hours (kWh).
One kilowatt-hour is 1000 W of power used continuously for one hour of time.
Kilowatt-hours are units of energy, not power!
Electric companies sell energy

## Slide 51
An important concept to remember:
kilowatt-hours is a unit for energy, not power.
Kilowatt-hours are energy units

## Slide 52
The average household is billed for around 500 kWh of electricity usage per month. What is the average power consumed for a household?
Electric power and energy
An important concept to remember:
kilowatt-hours is a unit for energy, not power.

## Slide 53
The average household is billed for around 500 kWh of electricity usage per month. What is the average power consumed for a household?
Electric power and energy
An important concept to remember:
kilowatt-hours is a unit for energy, not power.
This corresponds to nearly seven 100 W bulbs on continuously for the entire month!
Notes: Reinforce the idea that this is an AVERAGE rate. Usage varies. Sometimes we may have many appliances on at once. When we are away from home or everyone is asleep, usage may be much lower.

## Slide 54
Compile a list of the major appliances in your home.
Determine the power consumption of each one.
If they are all on at once, how much power do they use?
How much current does this correspond to?
check labels on the side or back of each appliance;
look up the power in the appliance manual; or
find the appliance model and look online for its power rating.
Home energy use
How much power do your home appliances consume? much

## Slide 55: Assessment
How much current flows through an incandescent light bulb that draws 40 W of power from a 120 V outlet?

## Slide 56: Assessment
How much current flows through an incandescent light bulb that draws 40 W of power from a 120 V outlet?

## Slide 57: Assessment
Two 30 Ω resistors are connected in series to a 120 volt outlet.
  How much current flows through the circuit?
  What is the power output of this circuit?

## Slide 58: Assessment
Two 30 Ω resistors are connected in series to a 120 volt outlet.
  How much current flows through the circuit? 2.0 amps
  What is the power output of this circuit?

## Slide 59: Assessment
Two 30 Ω resistors are connected in series to a 120 volt outlet.
  How much current flows through the circuit? 2.0 amps
  What is the power output of this circuit? 240 watts

## Slide 60
Two 30 Ω resistors are connected in parallel to a 120 volt outlet.
  How much current flows through the circuit?
  What is the power output of this circuit?
Assessment

## Slide 61: Assessment
Two 30 Ω resistors are connected in parallel to a 120 volt outlet.
  How much current flows through the circuit? 8.0 amps
  What is the power output of this circuit?

## Slide 62: Assessment
Two 30 Ω resistors are connected in parallel to a 120 volt outlet.
  How much current flows through the circuit? 8.0 amps
  What is the power output of this circuit? 980 watts

## Slide 63: Assessment
How many kilowatt-hours are consumed by a 100 W incandescent light bulb if it is left on for an entire day and night?

## Slide 64: Assessment
How many kilowatt-hours are consumed by a 100 W incandescent light bulb if it is left on for an entire day and night?
  Start with the power equation. Solve for energy by multiplying by time.

## Slide 65: Assessment
How many kilowatt-hours are consumed by a 100 W incandescent light bulb if it is left on for an entire day and night?
  Calculate, making sure to convert units to kilowatts and hours:
  Start with the power equation. Solve for energy by multiplying by time.